## Slide 1: Wind Power
Notes: Raise your hand if you use electricity. We are going to try and clarify what electricity is, how we measure it, and look at one alternative energy source for generating electricity, namely Wind.
<number>

## Slide 2: What is Electricity?
Electricity is the transport of energy through the motion of electrons
**We do not make electricity, we CONVERT other energy sources into electrical energy**
Notes: <number>
Electricity is defined as the energy transported by the motions of electrons. Usually through wires, right? But electricity cannot just be “made” instead we must convert it through other forms of energy. But how do we do that?

## Slide 3: How can we generate electricity?
a coil of wire is rotated in a magnetic field. When this happens, a voltage is produced in the coil!
This is called Induction.
Magnet
Coil of wire
Many different forms of energy are often converted into mechanical energy that is then converted into electricity.
Notes: See if your students can brainstorm and suggest several forms of energy that is converted into mechanical energy and then into electrical energy. Two common suggestions are hydroelectric energy and wind energy.
When you have a magnet in the middle of a coil- when either of them move it creates a voltage, or an electrical current. You can have either a moving wire, or a moving magnet which causes minute pushes and pulls on the electrons in the wire, causing them to move on down the line… thus creating an electrical current.
<number>

## Slide 4: Electric Generator
G
Mechanical
Energy
Electrical
Energy
Notes: <number>
So we have what are called generators, which convert what’s called mechanical energy- into electrical energy by having a coil rotate around a magnet.

## Slide 5: But how do we get the coil to rotate?
Pressurized Steam Turbines
    Burning fossil fuels to heat water into steam
    Nuclear – high temperatures to make steam
Hydroelectric
  Falling water has energy,
  which spins turbines
Wind!
  Moving air molecules have energy, too!
Notes: But how do we get these coils to rotate and create electricity? Well there are many different ways. We have what are called steam turbines, where you either burn fuels or use nuclear plants that make heat to warm up water into steam and turn turbines. Then there is what’s called hydroelectric power, where you use turbines spinning from the weight of falling water. Who here has seen a dam? Well inside those dams are giant turbines that are designed to turn a coil and induce electricity. Lastly, there is wind power! Using large blades, windmills catch the wind and turn a coil inside the windmill- again inducing electricity!
<number>

## Slide 6: How do we measure electrical energy?
Any energy is measured in Joules (J)
Voltage (V)
  Stored energy
Current (I)
  Flowing energy
Power
  Product of the two (V*I) , measured in Watts (W) , which is Joules per second (J/s)

## Slide 7
Oregon supplies over 1,000 megawatts
1 megawatt is enough power to supply 1,000 homes
Notes: <number>
Here is a diagram of all the windmills in the U.S. As you can see Oregon is a big contributor.

## Slide 8: Large Wind Turbines
Notes: So what do windmills actually look like? You can see here that they go up to 400 ft tall, and there blades are nearly 150 ft long!!
<number>

## Slide 9: Why do windmills need to be high in the sky?
High above the ground, winds are faster and more consistent.
Notes: <number>

## Slide 10: Parts of a Wind Turbine
Notes: <number>

## Slide 11
Notes: So here is a diagram of how the wind pushes the blades, and rotates a coil.
<number>

## Slide 12: Wind farms can also be offshore!
Wind is often stronger and more consistent out in the ocean.
Notes: <number>

## Slide 13: Make Your Own!
Notes: This is a fancier version than we will be making, but it applies the same aspects of design.
<number>

## Slide 14: What to do…
Each group is going to build their own wind turbine.
Design your own set of blades for the hub.
Cut them out and attach to the wooden dowels.
Make the hub spin using one of the electrical box fans.
Use the multi-meters to measure the mA (milli-amps) that you are creating and the mV (microvolts). Fill out the table, compare the two blade designs in your group and determine which set of blades is generating more power.
Remember to record your data on the worksheet provided.
Notes: <number>

## Slide 15: Photo Credits
Wind Farm in England. (2006, May 31). In Everblue. Retrieved August 9, 2011, from Google
HowStuffWorks. N.p., 2003. Web. 10 Aug. 2011.
Everblue. N.p., n.d. Google. Web. 10 Aug. 2011. <http://www.destination360.com/north-america/us/nevada/las-vegas/hoover-dam>.
"LLLJP Wind Turbine." NOAA ESRL CSD. N.p., n.d. Google. Web. 11 Aug. 2011. <http://www.esrl.noaa.gov/csd/projects/lamar/windturbine.html>
"The Scoop on Vertical Axis Wind Turbines, Part II." Mother Earth News. Ogden Publications, May 2009. Google. Web. 11 Aug. 2011. <http://www.motherearthnews.com/Energy-Matters-Vertical-Axis-Wind-Turbines-Debate.aspx>
"How Wind Turbine Works." Windbird. Wordpress, n.d. Web. 11 Aug. 2011. <http://windbrid.com/wind-energy_how-wind-turbine-works.html>.
Merchant, Brian. "Offshore Windfarms to Power 1/5th of Europe by 2030." Tree Hugger. Discovery, 14 Sept. 2009. Google. Web. 11 Aug. 2011. http://www.treehugger.com/files/2009/09/offshore-wind-farms-europe.php
"Recyclable Wind Turbine Keeps Engergy Green." Product Sourcing. N.p., 30 Apr. 2011. Google. Web. 11 Aug. 2011. <http://www.jihsin.com/manufacturers/recyclable-wind-turbine-keeps-energy-green.html>

## Slide 16
Credits and
Appreciation
Funding for this project was generously provided by a grant from the Oregon Engineering Technology Industry Council (ETIC) through the Oregon Pre-Engineering & Applied Sciences (OPAS) initiative.
Kidwind served as a great resource for our educational materials on alternative energy. Their web site is Kidwind.org.
Center for Outreach in Science and Engineering for Youth (COSEY) is a collaboration between the colleges of Science and Engineering and Precollege Programs at Oregon State University.