## Slide 1: How GPS works
Supplemental slides
Notes: Additional resources
https://www.scientificamerican.com/article/how-do-gps-devices-work/

## Slide 2
Notes: From https://www.gps.gov/systems/gps/space/
GPS fly in a medium earth orbit. There are 31 GPS (USA), > 60 GNSS satellites in orbit (2019)
GNSS - Global Navigation Satellite System (GPS being one of these, others include the Russian GLONASS, European GALILEO and Chinese BeiDou systems).

## Slide 3
Notes: The location of each satellite is known to a high precision.
They are tracked with radio to know their position. Which is why the most accurate GPS position requires ephemeris data, which provides the corrected position from the forecast track from the radio tracking.
Each satellite transmits a time signal and orbital data, at a synchronised time, to earth.
A GPS receiver computes it’s location based on arrival time of the signal (relative to when it was transmitted) and the known location of the satellite.
You need at least four satellites to trilaterate a position on Earth and estimate the precision of that position estimate. That is because there are 4 unknowns (receiver position = 3 coordinates in space, plus time)
From https://timeandnavigation.si.edu/multimedia-asset/how-does-gps-work

## Slide 4: First calculate distance to satellite
Hint:
Distance = Speed x Time taken
Remember: We can measure time accurately, satellites have an atomic clock, and the transmitted message is the time it was transmitted.
Speed is the speed of the radio signal, the speed of light.

## Slide 5: First calculate distance to satellite
Calculating time taken for the transmitted radio signal to be received requires that we know the time the signal is received.
Each satellite and receiver has a coded signal that repeats from the same time. These signals are matched to find time from transmission to receipt.
Notes: From https://www.quora.com/How-is-the-distance-between-a-GPS-device-and-a-GPS-satellite-calculated
However, note it is hard to follow the description here because the reason for why a sphere of possible locations for the receiver exist.

## Slide 6: First calculate distance to satellite
The receiver clock is inaccurate, which means the error on time received equates to a sphere around the receiver.
Four or more spheres are needed to find an intersecting point, which is the location of the receiver.

## Slide 7
Trilateration: Finding location by measuring distances.
3-D
2-D
Notes: Triangulation: Find location by measures angles to target from 3 or more locations.
Tralateration: Measures distances
https://gisgeography.com/trilateration-triangulation-gps/
We can estimate a distance to each satellite. On a 2-D plane this distance will trace out a locus of points on a circle. In 3-D this distance is on a sphere surrounding the satellite. If there are 2 satellites, with intersecting spheres, the reciever has to be located along the intersection of the two spheres. In 2-D this intersection is 2 points, adding another satellite reduces the intersection to 1 point.

## Slide 8
Notes: https://www.e-education.psu.edu/natureofgeoinfo/book/export/html/1796

## Slide 11
As we know roughly where we are, one possible solution (position) can be thrown out

## Slide 12
To estimate time of signal receipt, we need a 4th satellite.
Time to signal transmission is the same for all 4 satellites, but is unknown.
The location and time can be solved for with 4 simultaneous equations: a system of equations,
that has 4 unknowns, space (x,y,z) and time (t).

## Slide 13: Increase accuracy
Relativity dictates that time is faster in orbit, so this needs to be corrected for mathematically.
Atomic clock error is of the order of a nanosecond, which equates to about 2m error in distance to earth.
The atmosphere slows light down (air refracts light)
There are ways to correct for these time errors using a second receiver.

## Slide 14
For tracking sea ice we use similar GPS to that in your phone.
These GPS typically have an absolute position error of +/- 25m (for 95% of data).
For the application of tracking ice drift a 25m position error is acceptable.