## Slide 1: Wave Power
Photographer: Jason Childs/Getty Images
Notes: Raise your hand if you use electricity. What do you use electricity for?
We are going to try and clarify what electricity is, how we measure it, and look at one alternative energy source for generating electricity, namely Waves.
<number>

## Slide 2
Energy 101: Marine and Hydrokinetic Energy
Notes: https://www.youtube.com/watch?v=ir4XngHcohM
<number>

## Slide 3: Different kinds of Wave Energy Conversion (WEC) Devices
Oscillating Water Column
Attenuator
Overtopping
Point Absorber
Notes: There are four different “families” of Wave Energy Conversion Devices –
Oscillating Water Column
Attenuator
Overtopping
Point Absorber
<number>

## Slide 4: Oscillating Water Column WEC Devices
Notes: These devices generate power when a wave causes the water column to rise and fall pushing air through a fan which turns a generator.
An example size would be put into 20-100 foot depths and may be 65 feet wide.
<number>

## Slide 5: Oscillating Water Column WEC Devices
Notes: The Wavegen OWC is located on the Island of Islay in Scotland.
<number>

## Slide 6: Attenuator WEC Devices
Notes: These devices are oriented in the direction of incoming waves that cause articulated components to bend and drive generators.
This device is around 390 feet long and 11 feet wide with 7 feet above the surface of the water
<number>

## Slide 7: Attenuator WEC Devices
Notes: The Pelamis Attenuator device is located in Scotland.
It is 150 meters long, 3.5 meters wide and has four segments.
<number>

## Slide 8: Overtopping WEC Devices
Notes: These devices have a partially submerged structure that funnels waves over the top into a reservoir. The water runs back to the sea powering a low-head hydropower turbine.
An example prototype is roughly 100 by 200 feet, but may be scalable as large as 700 feet by 1,200 feet and 65 feet wide.
<number>

## Slide 9: Overtopping WEC Devices
Notes: The Wave Dragon is located off the coast of Denmark
22,000 tons
260x150meters, 16 meters high
<number>

## Slide 10: Point Absorber WEC Devices
Notes: These devices capture energy from the “up and down” motion of the waves. They may be fully or partially submerged.
<number>

## Slide 11: Point Absorber WEC Devices
Notes: The OSU/CPT Point Absorber is a buoy designed by OSU, Columbia Power Technologies, and the Navy.
23 feet tall, 11 feet wide
<number>

## Slide 12
Notes: Today, we are going to create our own Wave Energy Converter device. To which family does it belong?
This is a miniature Point Absorber Wave Energy Converter Device. But before we do that, we need to understand what electricity is. What is electricity?
<number>

## Slide 13: What is Electricity?
Electricity is the transport of energy through the motion of electrons
**We do not make electricity, we CONVERT other energy sources into electrical energy**
Notes: <number>
Electricity is defined as the energy transported by the motions of electrons. Usually through wires, right? But electricity cannot just be “made” instead we must convert it through other forms of energy. How do we do that?

## Slide 14: How can we generate electricity?
KINETICENERGY
MECHANICAL ENERGY
ELECTRICITY
Notes: Kinetic energy from a wave is converted to mechanical energy (the device moving up and down) which is then converted to electricity. But how?
<number>

## Slide 15: Electromagnetic Induction
MECHANICAL ENERGY
ELECTRICITY
A magnet has two poles.
When the magnet is moved between a coil of wire, it “excites” the electrons, making them move.
This creates a current (electricity!)
This is called Induction.
Magnet
Coil of wire
Notes: <number>
In our device, the Mechanical Energy of the moving buoy moves a magnet up and down inside a coil of wire.
As you know, magnets have two poles – a south pole and a north pole. Opposites attract, like poles repel. When a magnet is moved down the middle of a coil of wire, the polarity of the magnet causes the electrons in the wire to move about, creating a current of electrons – or electricity!
This process is called Electromagnetic Induction, or induction for short.

## Slide 16: Make Your Own!
Notes: Now it is time for us to make our own!
<number>

## Slide 17: Voltage Produced
There are many factors in this experiment that affect the amount of voltage produced. Can you think of any?
Number of turns in the coil
Length of coil
Diameter of the coil
Clearance between the magnet and the inside of the test tube
Strength of the magnet
Length of the stroke of the magnet
Speed of the magnet through the coil
Notes: Factors:
Number of turns in the coil – the higher the number, the more electrons available to move and create electricity
Length of coil – As the coil is “stretched out” with the number of turns remaining the same, the voltage will be reduced
Diameter of the coil – as the diameter of the coil grows larger, the voltage will be reduced
Clearance between the magnet and the inside of the test tube – as clearance is reduced, fluid friction with the water is increased and the magnet speed and voltage are reduced
Strength of the magnet – as the magnet gets stronger, so does it’s magnetic field, creating a stronger affect on the electrons in the coil
Length of the stroke of the magnet through the coil – this is controlled by wave height
Speed of the magnet through the coil – this is controlled by wave period.
<number>

## Slide 18: Experiment Variables
After your initial design, determine what variable you will change for each trial.
  A variable is what you change between tests
  Changing a variable will tell you what works & what doesn’t
Remember, only change one variable at a time
Challenge yourself to make predictions!
Notes: A variable in an experiment is anything that can be controlled or changed in an experiment.
<number>

## Slide 19
Credits and
Appreciation
The Northwest National Marine Renewable Energy Center (NNMREC) served as a great resource for wave energy. Their web site is nnmrec.oregonstate.edu.
Center for Outreach in Science and Engineering for Youth (COSEY) is a collaboration between the colleges of Science and Engineering and Precollege Programs at Oregon State University.
Notes: <number>